## Slide 1: a CEA/IRFM code for the evaluation of power deposition on ITER WALLS
First uses for ITER design studies:
  Protection of the leading edges of the ITER outer vertical target during downwards VDE
  Heat loads on the first wall for ICRF heating optimized plasma
  Heat loads on the gaps inside the W-monoblocks
  Heat loads to the upper first wall panels during the plasma ramp-down
  PFCFLUX code, developed from experiences on shadowing and heat flux simulation at IRFM, has been successfully installed and used at ITER.
Shadowing pattern
3D incident energy flux density distribution
einc –chamfer max ~ 43 MJ/m²
einc –flat max ~ 7 MJ/m²
leading edges fully protected
einc (MJ/m2)
  PFCFLUX is now intensively used for the preparation of the coming Final Design Review of the ITER W-divertor.